Lab 2 – Report - Sketch
Part 2 – Exp1 – Configure an IP Network

What are the ARP packets and what are they used for?

The Address Resolution Protocol (ARP) is a telecommunication protocol used for resolution of network addresses into link layer addresses. More specificaly, the ARP converts an IP address to a physical address such as a MAC address.
A table called the ARP cache is used to keep a correlation between each MAC address and it's corresponding IP address.
When an incoming packet arrives at a gateway, the gateway asks the ARP program to find a physical host (MAC address) that matches the IP address. The ARP check the ARP cache for a reference to that address and if it is found provides it so the packet can be converted to right format. However, if no match is found, the ARP broadcasts a request to all the machines on the LAN to see if one machine recognizes that it has that IP address associated with. If a machine replies, then the ARP cache is updated for future reference and the packet is sent to that machine.